## Slide 1: Diagnostic Hardware
PET
  Built in diagnostics on 2001
  The PETvet
VIC-20
  Commodore Diagnostic
C64 / C128
  Dead Test Cartridge (Really Useful)
  Other Diagnostic Cartridge
Plus/4, C16, C232
  Diag264

## Slide 2: PETvet
Developed By Mike Hill
Programmable ROM/RAM replacement
Customisable Memory Maps
Reprogrammable by Serial port
Tools to halt CPU and view memory

## Slide 3: Other PET Tools
Built in diagnostics on Rev-1 ROM’s
LED on board 2001 series
Build a NOP generator
The 2001 Service Kit!

## Slide 4: DiagPET / PETvet
Replaces the top 1k ROM (FC00-FFFF)
Installs ROM at A000 (normally unused)
Checks all RAM/ROM, including ZP/Stack

## Slide 5: VIC-20 Diagnostic
Commodores own tool
External ROM with own RAM

## Slide 6: VIC-20 Diagnostic
RAM / ROM Checksums
Primarily for I/O
Loop Backs most ports
Picture Courtesy Ray Carlsen

## Slide 7: C64 / C128 – Dead Test Cart
Ultimax mode to bypass Kernal
Works with no RAM/ROM/SID or CIA’s
Uses border to indicate bad RAM

## Slide 8: C64 / C128 – Diagnostic Cartridge
Needs a bootable machine
Like VIC cart, loops back I/O ports

## Slide 9: C64 / C128 – Diagnostic Cartridge
Easy to build your own
Schematics freely available, but over complicated!
C128 Version similar but untested by me.

## Slide 10: Plus/4, C16, C232 – Diag264
Built to fix a Commodore 232
Kernal or Cartridge based
Comprehensive testing of RAM/ROM & Ports

## Slide 11: Common Culprits - PET
Mostly ROM & RAM
  6540 / 2316 adapters from Jim Brain
  2114’s and 4116’s still plentiful (later 2001’s
  6550’s are tricky!
Decoding Logic (use a NOP generator)
  Standard 74 series TTL
Occasionaly CPU or VIA’s / PIA’s, but rarely
  WDC Still makes 6502’s

## Slide 12: Common Culprits – VIC 20
Reliable, mine all work today with no fixes!
ROM’s easily replaceable
RAM’s easily sourceable (2114’s, TMM2016)

## Slide 13: Common Culprits – C64
64’s are cheap, so by implication…
Most commonly PLA (black screen)
…& SID (works but defective sound)
CIA’s are fragile but replaceable
For everything else, Ray Carlsen…

## Slide 14: SuperPLA Multi
Created by Jens Schoenfeld
Extracted C64 PLA eprom image in 1994
Equations derived as part of C-One project
Implemented on a MACH210 modern PLA
Includes PLA’s from CBM-II’s, Plus/4, and 1551
Also includes modes not implemented on C128

## Slide 15: Resources
PET
http://www.bitfixer.com/bf/petvet
http://www.6502.org/users/andre/petindex/index.html
http://www.zimmers.net/anonftp/pub/cbm/pet/index.html http://www.vintage-computer.com/vcforum/forumdisplay.php?21-Commodore
VIC-20
http://sleepingelephant.com/ipw-web/bulletin/bb/index.php
C64, C128
http://www.retro-donald.de/pages/superpla-multi.php
http://www.swinkels.tvtom.pl/swinsid/
http://www.lemon64.com/
http://personalpages.tds.net/~rcarlsen/
Plus/4, C16, C232
http://inchocks.co.uk/commodore/Diag264/HTMLManual/Diag264.htm
http://plus4world.powweb.com/home http://www.commodore16.com/index.php/forum.html
Spares
http://www.arcadecomponents.com/index.html http://store.go4retro.com/ http://retro-donald.de/sinchai-shop/
General Info
http://www.softwolves.pp.se/misc/arkiv/ http://personalpages.tds.net/~rcarlsen/ http://www.zimmers.net/anonftp/pub/cbm/